## Slide 1: Microservices Cloud Simulator (MCS)
Scalable, ESDL based, energy system simulator (GO-e WP3.3B)

## Slide 2: Energy system Microservices Cloud Simulator
A simulation framework to model energy systems described using ESDL
Independent development of calculation services per energy object
  Configurable boiler plate project as a starting point
Simulations run on a cloud cluster with scalable calculation services
Created for GO-e WP3.3B
Mark Vrijlandt, Ruduan Plug, Edwin Matthijssen
TUE: Bart van der Holst, Gijs Verhoeven, Koen Kok
TU Delft: Arjen van der Meer

## Slide 3: Overview
GO-e WP3.3B Goals
Microservices Cloud Simulator
  Develop calculation services
  Run a simulation
First simulation results

## Slide 4: GO-e WP3.3B goal
“Investigate by means of simulations how effective DSOs can activate flexibility from the built environment using various combinations of flexibility activation mechanisms to prevent congestion in Dutch distributions”
This requires many simulations for large energy systems:
  5 (networks per DSO) x 3 (DSOs) x 8 (Archetypical Neighborhoods) = 120 networks
  Evaluate different flexibility activation mechanisms
  Different scenarios for #flexible assets, weather, electricity prices in various markets
  Costly optimizations involved due large number of energy assets

## Slide 5: GO-e WP3 IT goals
Use ESDL to describe energy systems
Run simulations on a scalable (cloud) cluster
Independent development of calculation services
TUE focus on implementing calculation logic without worrying about:
  Cluster setup and deployment
  Communication between the different components
  Starting service calculations when needed during the simulation
  ESDL parsing
  Setup and writing to database and visualizing results
  Setup local testing of single calculation services with required infrastructure

## Slide 6: Microserves Cloud Simulator
Three main repositories
Simulation Orchestrator Start and manage simulations via a REST API FastAPI
Model Services Orchestrator Deploy and manage calculation service models on Kubernetes Python asyncio-mqtt, kubernetes python client
Calculation Service Generator Create calculation service boiler plate code from a configuration yaml file Cookiecutter, Jijnja2
1. and 2. are deployed on AKS
3. is used via ‘docker run’
1
3
2

## Slide 7: Development of Calculation Services
Define expected input and output data per calculation
Create boiler plate Python project (‘docker run’) which:
  Can be deployed on Kubernetes
  Parses ESDL to get attribute values and connected ESDL objects
  Contains I/O data classes with protobuf parsing
  Sends/receives lifecycle and data MQTT messages
  Starts calculations when all expected data has been received and sends output
  Writes to InfluxDB
  Closes down when simulation is done or terminated
  Local testing setup
Implement logic Local testing Push docker image to online repository
1
2
3

## Slide 8: GO-e calculation service configuration

## Slide 9: Boiler plate project
Implement logic: ‘model/calculation/service_calc.py’
  One function per calculation
  Receives and sends ‘model/io/io_data.py’ data objects (as in service configuration)
Local testing
‘test/start_local_infrastructure.sh’: mosquitto, influxdb, Grafana on Docker Desktop
`test/start_test_simulation.py’: mock simulation orchestrator and required input data:
    Creates test ESDL file
    Waits for ‘ReadyForProcessing’ from calculation service, sends ‘ModelParameters’ containing the ESDL file
    Sends ‘NewStep’ messages and required input data
run ‘main.py’ or ‘test/run_service_in_container.sh’: start the service model
Finally ‘deploy/build_and_push_image_ci_tno_dots_go-e.sh’

## Slide 10: Start Simulation
POST request:

## Slide 11: First simulation: POST body
{
"name": "simulation name",
"start_date": "2020-09-06 23:30:00",
"time_step_seconds": 900,
"nr_of_time_steps": 288,
"max_step_calc_time_minutes": 20,
"keep_logs_hours": 1,
"log_level": "info",
"calculation_services": [
{
"esdl_type": "ElectricityDemand",
"calc_service_name": "edemandservice",
"service_image_url": "ci.tno.nl/dots/go-e/edemand_service:12.0.0",
"nr_of_models": 1
},
{
"esdl_type": "EConnection",
"calc_service_name": "emsservice",
"service_image_url": "ci.tno.nl/dots/go-e/ems_service:129.0.0",
"nr_of_models": 10
},
{
"esdl_type": "EnergySystem",
"calc_service_name": "lvnetworkservice",
"service_image_url": "ci.tno.nl/dots/go-e/lv_network_service:4.0.4",
"nr_of_models": 1
},
{
"esdl_type": "Party",
"calc_service_name": "dsoservice",
"service_image_url": "ci.tno.nl/dots/go-e/dsoservice:5.0.0",
"nr_of_models": 1
},
{
"esdl_type": "PVInstallation",
"calc_service_name": "pvsystemservice",
"service_image_url": "ci.tno.nl/dots/go-e/pv-service:2.0.0",
"nr_of_models": 1
},
{
"esdl_type": "Battery",
"calc_service_name": "batteryservice",
"service_image_url": "ci.tno.nl/dots/go-e/battery-service:13.0.0",
"nr_of_models": 1
},
{
"esdl_type": "EnvironmentalProfiles",
"calc_service_name": "weatherservice",
"service_image_url": "ci.tno.nl/dots/go-e/weather_service:5.0.0",
"nr_of_models": 1
},
{
"esdl_type": "EnergyMarket",
"calc_service_name": "damarketservice",
"service_image_url": "ci.tno.nl/dots/go-e/da-market-service:6.0.0",
"nr_of_models": 1
},
{
"esdl_type": "HeatPump",
"calc_service_name": "heatpumpservice",
"service_image_url": "ci.tno.nl/dots/go-e/heatpump-service:14.0.0",
"nr_of_models": 1
}
],
"esdl_base64string"
}

## Slide 12: Deploy models
Parse ESDL file: which calculation services are needed
SO sends ‘DeployModels’ message with deploy information
Pull service images
Deploy models on Kubernetes
Connect to message broker, subscribe to messages from the Simulation Orchestrator
‘ReadyForProcessing’ back to SO
2
1
3
4
6
5

## Slide 13: Configure models
Distribute ESDL objects over calculation service models
SO sends ‘ModelParameters’ message containing the ESDL file and the list of ESDL id’s to perform calculations for in the model
Parse ESDL: subscribe to messages from connected assets, connect to influxdb
‘Parameterized’ back to SO
4
3
2
1

## Slide 14: Simulate time steps and clean-up
SO starts each time step with ‘NewStep’ message (start, duration, time step number)
Run each calculation when all input data is received
Send ‘CalculationsDone’ to SO . . loop 1,2,3 through all timesteps . .
When all time steps are finished SO sends ‘SimulationDone’ to all models
Each model writes to database
Calculation service model containers terminate
Clean up terminated pods after ‘log viewing’ period
3
2
1
4
5
7
6

## Slide 15: View progress and results
Check simulation progress (or terminate simulation)
View Grafana dashboards
View logs via Lens
3
2
1

## Slide 18: First simulation: Service overview
Low-voltage network (ESDL: energysystem)
Assets:
  Baseload (ESDL: Edemand)
  PV (ESDL: PVInstallation)
  Battery (ESDL: Battery)
  Heat pump (ESDL: HeatPump)
Energy Management system (ESDL: Econnection)
Weather (ESDL: EnvironmentalProfile)
Day-ahead market (ESDL: EnergyMarket)
DSO (ESDL: Party)
All in a Building

## Slide 19: Dynamic Bandwidth tariff
When the DA-prices were low, the DSO expected congestion (mainly due to batteries)
If the bandwidth is active, congestion can be prevented if the associated costs are high enough
But new congestion can occur in real-time
Load on the cable

## Slide 20: Abstract accepted

## Slide 21: Learnings
Cookiecutter works well for configurable code generation
  Jinja2 templating
  Pre- and post-gen hooks
  Setup to run in utility Docker container (also takes care of protobuf compile)
Good corporation with TU scientists: they can focus on python implementation
Reuse of existing component (Model Services Orchestrator) from another project with only a couple of changes and additions needed

## Slide 22: Ideas for future development
Move from ci.tno.nl to open source
Efficient update of existing calculation services (add/change IO data)
Currently all data communication goes via MQTT, for large datasets allow via database?
Run multiple simulations in a loop?
Cloud monitoring, put to sleep when not used
Automated testing of microservices
Incorporate S2 Flexibility Protocol for communication between energy objects
Build front-end for easier simulation management (calculation flow diagram) and viewing of results
Create library of services
Use Microservice Cloud Simulator (MCS) for other types of simulations consisting of different components
  Some changes needed in the ‘Simulation Orchestrator’ and ‘Calculation Service Generator’
Future projects: DEMOSES?, …

## Slide 24: Sequence diagram

## Slide 25: Sequence diagram: deploy

## Slide 26: Sequence diagram: configure

## Slide 27: Sequence diagram: simulation loop

## Slide 33: Dynamic bandwidth tariff
12:00
DA Closing
00:00
00:00
00:00
T
Expected Congestion moment
00:00
EMS 1
DSO
EMS n
Aggregate load prognosis for next day for each of the connected phases
Send aggregated loads for next day per phase to DSO
Perform load flow for next day, determine expected congestion problems, adjust bandwidth height* on congestion timesteps
EMS 1
…
Send updated bandwidth height to all connected EMS
EMS 1
EMS n
EMS 1
…
T
Expected Congestion moment
T
Expected Congestion moment
* DSO sends out bandwidth list for 96 timesteps :
If load flow indicates no congestion - > No bandwidth in place [ NaN, NaN, NaN, NaN , NaN, NaN … NaN ]
If load flow indicates congestion -> Bandwidth in place on timesteps of expected congestion [ NaN, 3000, 3000, NaN, 3000, NaN … NaN ]
T
Expected Congestion moment
T
Expected Congestion moment